## Slide 1: Software Engineering and VR
The Devil in the Details
Tom Forsyth
Software Architect, Oculus
Jan 27th 2015

## Slide 2: Tom Forsyth
Graphics drivers @ 3Dlabs
Game graphics @ Muckyfoot
  Urban Chaos
  Startopia
  Blade 2
Animation middleware: Granny3D @ RAD Game Tools
Instruction set design on Larrabee / Xeon Phi @ intel
VR @ Valve
  VR support on Team Fortress 2 & Half Life 2
Software Architect @ Oculus
  All things graphics
  Distortion & calibration, interacts with lens design
  Best practices, dev.rel. support, psychology

## Slide 3: VR is awesome!

## Slide 4: VR is awesome!

## Slide 5: VR is awesome!

## Slide 6: VR is awesome!

## Slide 7: VR is awesome!

## Slide 8: VR is awesome!

## Slide 9: VR is awesome!
VR is also incredibly tricky

## Slide 10: VR is awesome!
VR is also incredibly tricky
“Bleeding-edge realtime 3D graphics” is the easy bit
  Lots of hard stuff here of course, but needs an entire lecture series

## Slide 11: VR is awesome!
VR is also incredibly tricky
“Bleeding-edge realtime 3D graphics” is the easy bit
  Lots of hard stuff here of course, but needs an entire lecture series
VR adds so many other areas
  Display and optics
  Hardware diversity
  Time and latency
  Bugs that take a long time to manifest
  Interactions with user physiology
3

## Slide 12: VR overview
Hardware:
Screen
Lenses
IMU (gyro + accelerometer)
Camera & LEDs
(and lots of scary details!)
4

## Slide 13: VR overview
Software:
Tracking
Prediction
Rendering
Timewarp
Distortion & processing
(all timings are examples, not any specific device)

## Slide 14: Software in detail
Read 60Hz camera
  Find LED dots
  Find HMD pose from dot positions

## Slide 15: Software in detail
Read 60Hz camera
  Find LED dots
  Find HMD pose from dot positions
Read 1000Hz IMU: gyro + accel
Sensor fusion
  Last known-good camera pose
  Integrate IMU data forwards
    (this is the concept - in practice it’s a continuous filter)

## Slide 16: Software in detail
Read 60Hz camera
  Find LED dots
  Find HMD pose from dot positions
Read 1000Hz IMU: gyro + accel
Sensor fusion
  Last known-good camera pose
  Integrate IMU data forwards
    (this is the concept - in practice it’s a continuous filter)
Predict motion forwards to next frame display time
  Will typically be ~20ms away
6
20ms

## Slide 17: Software in detail
App renders view from each eye
  Typically takes a frame, i.e. 10-15ms
20ms

## Slide 18: Software in detail
App renders view from each eye
  Typically takes a frame, i.e. 10-15ms
Re-read latest IMU data and re-predict to next frame
  Prediction is now only ~5ms
  Timewarp
20ms
5ms

## Slide 19: Software in detail
App renders view from each eye
  Typically takes a frame, i.e. 10-15ms
Re-read latest IMU data and re-predict to next frame
  Prediction is now only ~5ms
  Timewarp
Image processing
  Distortion
  Chromatic aberration
  Compositing
  Gamma curve
  Overdrive
7
20ms
5ms

## Slide 20: Doing the timewarp
Reprojection of a rendered scene to a different orientation
  Rotational works well, positional less so
Three separate effects in one mechanism

## Slide 21: Doing the timewarp
Reprojection of a rendered scene to a different orientation
  Rotational works well, positional less so
Three separate effects in one mechanism
Late IMU read, re-predict, and fixup
  Smaller prediction time = much less error

## Slide 22: Doing the timewarp
Reprojection of a rendered scene to a different orientation
  Rotational works well, positional less so
Three separate effects in one mechanism
Late IMU read, re-predict, and fixup
  Smaller prediction time = much less error
Rolling shutter compensation
  The display lights up a line at a time, not all at once

## Slide 23: Doing the timewarp
Reprojection of a rendered scene to a different orientation
  Rotational works well, positional less so
Three separate effects in one mechanism
Late IMU read, re-predict, and fixup
  Smaller prediction time = much less error
Rolling shutter compensation
  The display lights up a line at a time, not all at once
Mitigation for stutters and stalls (“async timewarp”)
  Makes them less painful, but still look bad
  This does NOT mean you can render at 30fps!
9

## Slide 24: Sounds simple, what could go wrong?
VR brings some specific problems to the picture
Timing is critical
  VR relies on correct prediction
  Errors in timing are difficult to diagnose
Hardware configuration & variability
  GPUs
  Power management
  USB devices
Human variation
11

## Slide 25: Timing, timing, timing
Rendering uses a lot of predicted HMD poses
  Requires high-quality data to do good prediction
  Requires the actual display time to be within ~2ms of predicted
  Being an entire frame late or early (~12ms) is throw-against-wall bad

## Slide 26: Timing, timing, timing
Rendering uses a lot of predicted HMD poses
  Requires high-quality data to do good prediction
  Requires the actual display time to be within ~2ms of predicted
  Being an entire frame late or early (~12ms) is throw-against-wall bad
Incorrect timing is very difficult to see
  Even experienced people can’t reliably see <10ms errors
  But they will make people nauseous after 15mins
  “Works on my machine” isn’t even reliable!
  Most automated testing only does functionality, not timing
12

## Slide 27: Hardware configuration problems - GPUs
VR requires a fixed, consistent framerate
  Apps do not have fixed frame content
  Timewarp can help mitigate the worst stutters

## Slide 28: Hardware configuration problems - GPUs
VR requires a fixed, consistent framerate
  Apps do not have fixed frame content
  Timewarp can help mitigate the worst stutters
Massive range of performance in desktop PCs
  Multiple axes of perf: drawcalls vs compute vs bandwidth
  Any can be the limit for different parts of the scene

## Slide 29: Hardware configuration problems - GPUs
VR requires a fixed, consistent framerate
  Apps do not have fixed frame content
  Timewarp can help mitigate the worst stutters
Massive range of performance in desktop PCs
  Multiple axes of perf: drawcalls vs compute vs bandwidth
  Any can be the limit for different parts of the scene
GPU APIs & system optimized for throughput, not low latency
  Rendering pipeline has very low-quality timing feedback
  Use big hammers to solve – lots of stalls & syncs
  Wastes a lot of performance
17

## Slide 30: Hardware configuration problems - Clocks
CPU and GPU will throttle/overclock according to thermals
Precise CPU clock measures cycles – changes with frequency!
  Reliable “chipset” clock has coarse granularity
  We use one to sync the other - mostly works
  Finally fixed with Skylake CPUs – reliable AND precise
    But Skylake isn’t out yet…
Especially difficult on mobile & laptops
  Very aggressive throttling
  Perf will change mid-frame
16

## Slide 31: Hardware configuration problems - USB
Data collected by CPU polling
Hubs have unknown buffering granularity
  Every PC has multiple hubs in it, plus external ones
  Each adds unpredictable latency
USB devices can block each other (async isn’t that async)
HMD has a reliable clock, timestamps all events
  But we still have to sync up HMD and CPU clocks over USB
18

## Slide 32: Bug-fighting tools
Capture and reply of sensors
Robots & mo-cap
Motion-to-pixel tests
Feedback from HMD

## Slide 33: Capture and replay of sensor inputs
Outputs compared with known-good results
Good for sensor algorithm development
  Blob finding
  Pose estimation
  Fusion of IMU and vision
Good for nightly tests
  Easy to accidentally add noise, off-by-one-sample errors during dev
Good for performance tests
  Completely repeatable inputs
20

## Slide 34: Robots & mo-cap
Robot arm with HMD mounted on it
  Makes known & somewhat repeatable motions
  Tests hardware sensor error, noise, temperature, etc
Cube/room of professional mo-cap cameras
  Captures actual human movement
  Data is not as clean as you’d like – lots of filtering needed
Hard to run nightly or regression tests
  Slightly different every run
  Changing HMD or camera requires recalibration
  But we’re starting to try it
22

## Slide 35: Motion-to-pixel tests
Feed sensor-fusion outputs to rendering engine
Optional deterministic time stream
  Replace real clock with recorded one
Render & take screen captures

## Slide 36: Motion-to-pixel tests
Feed sensor-fusion outputs to rendering engine
Optional deterministic time stream
  Replace real clock with recorded one
Render & take screen captures
Comparing images is surprisingly difficult
  “No change” optimisations can easily cause small pixel/colour changes
  But are they correct changes or bugs? Requires operator skill
  Differences between GPUs, even between driver versions
  Bug fixes & new features require humans to re-approve new images
Still setting this system up – results TBD
24

## Slide 37: Feedback from HMD
HMD sends top-left pixel value back over USB, with timestamp
  Top-left pixel is beyond lens range, so we can use as a frame ID
  Dynamic end-to-end latency test of graphics system

## Slide 38: Feedback from HMD
HMD sends top-left pixel value back over USB, with timestamp
  Top-left pixel is beyond lens range, so we can use as a frame ID
  Dynamic end-to-end latency test of graphics system

## Slide 39: Feedback from HMD
HMD sends top-left pixel value back over USB, with timestamp
  Top-left pixel is beyond lens range, so we can use as a frame ID
  Dynamic end-to-end latency test of graphics system
  Used to fine-tune prediction algos
Useful for helping a user set up a working system
  Run simple Oculus test app, are you getting correct latency?
  Spots dodgy drivers, broken cables, USB problems, etc

## Slide 40: Feedback from HMD
HMD sends top-left pixel value back over USB, with timestamp
  Top-left pixel is beyond lens range, so we can use as a frame ID
  Dynamic end-to-end latency test of graphics system
  Used to fine-tune prediction algos
Useful for helping a user set up a working system
  Run simple Oculus test app, are you getting correct latency?
  Spots dodgy drivers, broken cables, USB problems, etc
Not as useful to a running app
  What can an app do with “latency is too high” message?
  Dynamic scaling of rendering speed has difficult hysteresis & feedback
    Still a hard research problem
26

## Slide 41: Bug-fighting methodologies
Naming schemes
Code standards
Multiple pairs of eyes
Unit tests / test-driven development
Asserts
Code reviews

## Slide 42: Naming schemes
Not that important, just pick one
  CamelCaps vs under_scores
  local/m_Member/g_Global
  szHungarian

## Slide 43: Naming schemes
Not that important, just pick one
  CamelCaps vs under_scores
  local/m_Member/g_Global
  szHungarian
We chose:
  CamelCaps
  localVar/MemberVar/GlobalVar
  no

## Slide 44: Naming schemes
Not that important, just pick one
  CamelCaps vs under_scores
  local/m_Member/g_Global
  szHungarian
Spaces and units – important!
  EyePos -> EyePosInHead
  Transform -> HeadFromWorld (see blog post for details)
  Delta -> VsyncDeltaMillisecs
  Brevity is not a virtue – take advantage of autocomplete!
We chose:
  CamelCaps
  localVar/MemberVar/GlobalVar
  no
28

## Slide 45: Code standards
In the sense of “which features of C++ do we use?”
Extremely effective

## Slide 46: Code standards
In the sense of “which features of C++ do we use?”
Extremely effective… at causing arguments
  Functional purists
  Template metacoders
  Inheritance-tree huggers
  Abstractionistas
  C99ers

## Slide 47: Code standards
In the sense of “which features of C++ do we use?”
Extremely effective… at causing arguments
  Functional purists
  Template metacoders
  Inheritance-tree huggers
  Abstractionistas
  C99ers
Conclusions fuzzy, but point towards using fewer language features
  Sometimes called “C+” (many variants)
  Fewer surprises, more typing
  But coders are really good at typing
30

## Slide 48: Multiple pairs of eyes
Bugs can be invisible to some, really obvious to others
  Always get others to check your visuals
  Learn what you can and can’t see

## Slide 49: Multiple pairs of eyes
Bugs can be invisible to some, really obvious to others
  Always get others to check your visuals
  Learn what you can and can’t see
Ten people can’t see a problem and one person can – it’s a problem
  There is no “authority” in these cases
  Deal with it the same way as colour-blindness (5%-10% of the pop)
  Designated guinea-pigs for each artifact

## Slide 50: Multiple pairs of eyes
Bugs can be invisible to some, really obvious to others
  Always get others to check your visuals
  Learn what you can and can’t see
Ten people can’t see a problem and one person can – it’s a problem
  There is no “authority” in these cases
  Deal with it the same way as colour-blindness (5%-10% of the pop)
  Designated guinea-pigs for each artifact
But sometimes you have to pick your battles
  60Hz/75Hz/90Hz low-persistence
  Fast-moving FPS games
  Screen door effect vs blur
32

## Slide 51: Unit tests / test-driven development

## Slide 52: Unit tests / test-driven development
Analysing…

## Slide 53: Unit tests / test-driven development
Analysing…
26/26 tests PASSED

## Slide 54: Unit tests / test-driven development
Very little help in subjective algorithm development
  Only work for refactoring and optimization
  We just don’t do that very much! VR does not have “big data”
  Not much use for GPUs
Actively impede algorithm development

## Slide 55: Unit tests / test-driven development
Very little help in subjective algorithm development
  Only work for refactoring and optimization
  We just don’t do that very much! VR does not have “big data”
  Not much use for GPUs
Actively impede algorithm development
I don’t like the bang for the buck
  Very few interesting bugs would have been caught with them
  Trivial ones easily caught by other methods
  Not worth the effort, complexity and maintenance
34

## Slide 56: Asserts
I love asserts
  Personal codebase – 20% LOC are asserts!
Double as documentation
  Cannot go out of date like comments and docs
  Especially on function arguments/inputs – ranges, allowed combos, etc
Can be used for mini unit tests

## Slide 57: Asserts
I love asserts
  Personal codebase – 20% LOC are asserts!
Double as documentation
  Cannot go out of date like comments and docs
  Especially on function arguments/inputs – ranges, allowed combos, etc
Can be used for mini unit tests
Almost nobody dislikes asserts
  Makes them almost unique amongst language features!
  Though many aren’t very aggressive about using them
Lots of nasty bug-hunts could have been caught early by asserts
36

## Slide 58: Code reviews
Cardboard-cutout-dog effect
  Just explaining it to someone else causes self-analysis
Increases “bus factor”
  Ownership = responsibility, not control. Tell people how your code works!
However, can be a time sink
  Leads to yes-men review-buddies
  Making it online, not in-person can help (but reduces CCD effect)
  Hard-and-fast rules create cheats – make it recommended not mandatory
Various cultures within Facebook & Oculus
  Different groups have different code review cultures
38

## Slide 59: Bug-fighting methodologies – score sheet
Naming schemes
Code standards
Unit tests / TDD
Asserts
Code reviews
Pick one, almost any one
Keep it simple
Nope
Yes yes yes
Maybe, but don’t go nuts
39

## Slide 60: …and that’s just the SDK!
Developing an app that uses VR has a bunch of other fun
All the usual complexity of realtime 3D rendering
Big performance requirements
  Mono@60o@30fps -> Stereo@100o@75fps (and that was last year)
Input restrictions (can’t see a keyboard)
Design restrictions
  Can’t force camera angles – must follow the user’s head
  Cinematic language reduced – framing, composition, angles, cuts
For more, see my GDC2014 talk
41

## Slide 61: VR is mean to brains
World scale is due to multiple cues
  Pupil separation and head motion must match physical user
    Or be a consistent scaling
  Height of virtual camera from ground
  Physical dimensions of in-game avatar
  Vergence vs focus conflict
  Floor-dragging effect – your feet overrule your eyes
Vestibular/optical mismatch – motion sickness
  Ears say you’re sitting still, eyes say you’re moving
  HW & SW working perfectly, but induces rollercoaster/travel/seasickness
43

## Slide 62: VR is mean to coders
Multiple bugs can look identical, e.g. “judder” can be:
  Framerate dropping below HMD rate
  Incorrect latency prediction
  Incorrect physics simulation time
  Misbehaving USB hubs
  GPU buffering/syncing (especially with multi-GPU)
  Misc other rendering bugs
Errors frequently “invisible”, but still cause nausea
  Extra frame of latency
  Off-by-one-pixel rendering
  Position tracking not working
  Swapped eyes (yes, really)
45

## Slide 63: VR is really mean to graphics
Much of our graphics intuition becomes useless
  Algorithms can be doing exactly what we want, yet feel terrible
Normalmaps look rubbish with stereo & head motion
  Looks like “hologram foil”
  Need high-quality, physically consistent disp.maps
Billboards and impostors have to be ~10x as far away
  Grass, leaves, mist, effects
Most specular methods don’t stereo-fuse properly
  …and specular that does fuse shows up surface triangle structure 
2D screenspace labels don’t work – need in-world 3D ones
47

## Slide 64: Conclusion
VR is all the hard things rolled into one
  Display and optics
  Wide range of hardware
  Time and latency
  Bugs that take a long time to manifest
  Interactions with user physiology

## Slide 65: Conclusion
VR is all the hard things rolled into one
  Display and optics
  Wide range of hardware
  Time and latency
  Bugs that take a long time to manifest
  Interactions with user physiology
But when it works it’s awesome
  Dumpy: Going Elephants
  Showdown demo by Epic
  Elite:Dangerous with a DK2 and HOTAS
49

## Slide 66
Questions?
developer.oculus.com
tom.forsyth@oculus.com
Further reading
Oculus dev area: Best Practices Guide
GDC / Connect 2014: Developing VR Experiences with the Oculus Rift
Personal blog: eelpi.gotdns.org/blog.wiki.html
Relevant entries: Matrix maths and names
Logging, asserts and unit tests